## Slide 1
Configuration Aerodynamics
- Classical Methods Applied
J. Philip Barnes
Northrop Grumman Aeronautics Systems
AIAA Aviation Forum, Reno NV, 16 June 2020
Copyright © by J. Philip Barnes
Published by the American Institute of Aeronautics and Astronautics, Inc., with permission.
Animated, annotated charts
with audio ; use F5 key
See also View ~ Notes Pages
Notes: The main objectives of Configuration aerodynamics are the shaping of the aircraft and computation of aero forces and moments. Until recent decades, classical and empirical methods were successfully applied to design, build, and fly. Today, we have a tendency to proceed directly to computational fluid dynamics. Although CFD provides superior detail, it often suffers much-reduced computational efficiency, far-greater user-setup time, copious global-warming emissions from banks of servers, and potentially-lesser understanding of its results if classical principles are forgotten. This presentation reviews, renews, and applies key principles of longitudinal configuration aerodynamics.

## Slide 2
Forebody
Configuration Aerodynamics – Classical Methods Applied
Theorists
GettyImages.com
Foil para. geom.
Apply
Emp. L’line
L. edge thrust
App. upwash
Elliptic wing
Sweep
Foil empirical
Wing empirical
Review and renew of classical principles & prelim. analysis of longitudinal configuration aero
Notes: Along the way we’ll visit with well-known and visionary theorists, including Ludwig Prandtl, Albert Betz, Max Munk, and Robert T. Jones. ● Our first topic is airfoil parametric geometry. ● We’ll then empirically characterize airfoil transonic lift and drag. ● Next, we’ll show that Prandtl’s elliptical-wing lift and induced drag calculations, although pioneering, are both optimistic by several percent. ● We’ll show improvements and extensions of wing lift slope provided by Helmbold, Diederich, and Polhamus. ● Then we review and renew the discoveries of Munk and Jones on forebody aerodynamics, ● progressing from there to study wing-body aerodynamics with our empirical lifting line. ● Next we review sweep theory and data, ● introduce a new empirical characterization of airfoil leading-edge thrust, ● and describe our apparent-upwash method to evaluate drag due to lift. ● Finally, we’ll apply the methods to study the top-level aerodynamics of one or more new and unique configurations.

## Slide 3
Forebody
Configuration Aerodynamics – Classical Methods Applied
Theorists
GettyImages.com
Foil para. geom.
Apply
Emp. L’line
L. edge thrust
App. upwash
Elliptic wing
Sweep
Foil empirical
Wing empirical

## Slide 4
New or Existing airfoil parametric geometry via the cubic spline
X(u) parameterization
Z(u) cubic spline with
flat, slope-set, stiff, or
flexible end controls
Example:
1-pt. upper
2-pt. lower
L.E. radius
Aft b0 ; b1
Powerful, rapid definition of smooth geometry for existing or new airfoils
Z’ = -p R0.5
Z’ = p tanb
Notes: The cubic spline is a powerful numerical tool and classic application of calculus, solving a linear system of equations to characterize and interpolate a smooth curve. While preserving continuity of first and second derivatives at each internal knot, we set at each independent end either a flat or finite slope, or a condition of either stiffness or flexibility. ●
The cubic spline can efficiently describe airfoil geometry with a parameter (u) ranging from zero to one, counter-clockwise from the upper trailing edge. ● Here, we first parameterize X(u) ● and then fit a spline Z(u). The slopes in the middle and at each end ● are related to the leading-edge radius and afterbody slopes. ● This allows us to powerfully describe a new or existing airfoil, in this case the FX66, with just two lower points and one upper point. ●
....
Those interested can explore what we might get by declaring only the leading-edge radius and upper/lower afterbody angles.

## Slide 5
Forebody
Configuration Aerodynamics – Classical Methods Applied
Theorists
GettyImages.com
Foil para. geom.
Apply
Emp. L’line
L. edge thrust
App. upwash
Elliptic wing
Sweep
Foil empirical
Wing empirical

## Slide 6
NACA high-speed test data: Transonic Lift Slope - Interpreted
Blended interpretation with theoretical bounds
MaryEvans.com
Notes: Transonic wind-tunnel test data for airfoil lift and drag varies notoriously by report and by facility, in large part due to the difficulty of collecting such data. This requires us to interpret the consensus of the data. Here we characterize NACA test data for airfoil normalized lift slope versus thickness and Mach number, with the family of curves bounded subsonically by Prandtl-Glauert theory.

## Slide 7: Symmetric airfoil transonic drag rise
Pressure drag (cdp) is the excess over the friction drag (cdf) ”floor”
Notes: This plot characterizes symmetric airfoil drag at zero lift versus thickness and flight Mach number. We’ll revisit this plot when we study the effects of sweep.
...
Supersonically, the curves have been faired into circular-arc airfoil theory.

## Slide 8
Forebody
Configuration Aerodynamics – Classical Methods Applied
Theorists
GettyImages.com
Foil para. geom.
Apply
Emp. L’line
L. edge thrust
App. upwash
Elliptic wing
Sweep
Foil empirical
Wing empirical

## Slide 9
Prandtl’s elliptical wing: “Pure” lifting line over predicts lift
cL(A+2h)/( 2pAh)
Equivalent-plate Incidence, (a+z)o
Prandtl Theory
cL = 2ph (a+z) A /(A+2h)
Evaluating both lift & downwash at quarter-chord overpredicts lift
h ≡ (dcl /da) / (2p)
Data
Notes: We are indebted to Ludwig Prandtl for a pioneering analysis of wing lift slope. ● However, he modeled the wing and its wake with a “pure” lifting line, by evaluating both lift and downwash at one-quarter-chord. Such modeling led to a typical 10% overprediction of lift. ● Follow-on researchers instead adopted a “lifting surface” approach by adding a downwash line at three-quarter chord, and that brought us much closer to test data as we show next. ●

## Slide 10
Forebody
Configuration Aerodynamics – Classical Methods Applied
Theorists
GettyImages.com
Foil para. geom.
Apply
Emp. L’line
L. edge thrust
App. upwash
Elliptic wing
Sweep
Foil empirical
Wing empirical

## Slide 11
Unswept Wing Lift Slope Data & Theory ~ Heinrich Helmbold
J. Philip Barnes, April 2013
h ≡ (dcl /da) /2p ≈ 0.95
Notes: German aerodynamicist Heinrich Helmbold improved upon Prandtl’s wing analysis ● by applying a lifting-surface model. ● In the NACA low-speed test data seen here for a wide range of unswept wings, Helmbold’s model comes closer to the test data. In addition, Helmbold’s method falls into agreement with test data and R.T. Jones’ prediction at very low-aspect-ratio. ●

## Slide 12
Helmbold-Diederich Condensation: Low-speed Lift Slope
h ≡ (dcl /da) /2p
Notes: Frederick Diederich, an American aerodynamicist at NACA, extended Helmbold’s low-speed lift-slope formula to include mid-chord sweep. Diederich introduced a “normalized lift slope” and “equivalent aspect ratio” (F) with which low-speed lift-slope data for a wide range of wing shapes collapses to a single broad-brush curve which we call the Helmbold-Diederich Condensation. Diederich’s formula reduces to Helmbold’s when sweep is zero.

## Slide 13
Helmbold-Polhamus Condensation: Subsonic lift slope
No effect of Mach as A→0 ; Consistent with R.T. Jones
h ≡ (dcl /da) /2p
Notes: An extension of wing lift slope characterization, now accounting for sweep and subsonic transonic effects, was provided by NACA aerodynamicist Edward Polhamus. Here, lift slope at an equivalent aspect ratio (E) is normalized to the Munk-Jones low-aspect-ratio reference. This Helmbold-Polhamus Condensation, representing all the wings shown here, is consistent with R.T. Jones’ theory predicting no effect of Mach number on lift slope as aspect ratio approaches zero. ● Polhamus’ formula reduces to Helmbold’s at zero sweep and zero Mach number. ●

## Slide 14
Forebody
Configuration Aerodynamics – Classical Methods Applied
Theorists
GettyImages.com
Foil para. geom.
Apply
Emp. L’line
L. edge thrust
App. upwash
Elliptic wing
Sweep
Foil empirical
Wing empirical

## Slide 15
Forebody Aerodynamics ~ Max Munk
Definitions
A  aspect ratio, b2/S
a  angle of attack
b  base width, “span,” or diam.
f  fwd distance, base-to-AC
L  lift force
M  pitching moment at base
n  forebody “nose” length
q  flight dynamic pressure
S  forebody planform area
  forebody volume (axi-sym.)
w  local width, “span,” or diam.
x  axial coord., aft of body apex
b
w
f
M
L
n
x
From NACA TN 207 (Munk):
M = 2 q a  [1]
dL/dx = p a q w dw /dx [2]
Integrate [2]:
L = 2 q a (p/4) b2 [3]
cL  L/(qS) = (p/2) A a [4]
We extend Munk’s work
to obtain the AC position:
M = f L [5]
Combine [1, 3, 5]:
f/n = 4 /(nb2) (axi-sym)
= 05/15 (conic)
= 08/15 (parabolic)
= 10/15 (elliptic)
Max M. Munk
These have the same lift
Notes: The mercurial Max Munk, arguably Prandtl’s most gifted "theoretically-minded" protégé, authored numerous important technical papers on monoplanes, biplanes, and thin airfoils. He was deservedly proud of his papers, so much so that in WWI he ensured their "leakage" across the channel, before the authorities could stamp his work secret.
Munk’s work after WWI, now on behalf of the Allies, included studies of airships at incidence. ● Munk showed that an axisymmetric forebody’s pitching moment ● is proportional to its volume, ●● and its lift is proportional to the square of its base diameter (b). ● Given both the lift and pitching moment, we can expand upon Munk’s results to compute the forebody aerodynamic center position ● for conic, parabolic, and elliptical forebodies. ●

## Slide 16
Low-aspect-ratio wing aerodynamics ~ Robert T. Jones
Student of Max Munk
No formal degree
Low-A delta wings
Supersonic aero
Classic NACA papers
Robert T. Jones
NACA TN 1032 (Jones):
dL/dx = p a q w dw /dx
L = 2 q a (p/4) b2
cL  L/(qS) = (p/2) A a
cDL  cL a/2 = cL2/(pA)
Definitions
A  aspect ratio, b2/S
a  angle of attack
b  base “span”
D  drag ; L  lift
q  flight dynamic pressure
S  forebody planform area
w  local width
x  axial coord., aft of apex
b
L
x
D
Looking fwd and inboard
w
Ph.D not required
No Mach effect on cL ; cDL
Notes: Robert T. Jones, famed NACA aerodynamicist, was a student of Max Munk in the U.S. ● With no formal degree, Jones went on to publish many significant technical papers at NACA, with one on the lift and drag of low-aspect-ratio wings. ● After independently duplicating Munk’s finding that lift is proportional to the square of the span (b), ●● Jones went beyond his teacher on this topic by computing the drag, remarkably obtaining the same formula for induced drag as that obtained by Prandtl for higher aspect ratios, ● and by showing that Mach number has no effect on forebody lift or drag coefficients. ● ●

## Slide 17
Forebody
Configuration Aerodynamics – Classical Methods Applied
Theorists
GettyImages.com
Foil para. geom.
Apply
Emp. L’line
L. edge thrust
App. upwash
Elliptic wing
Sweep
Foil empirical
Wing empirical

## Slide 18
“Wingman”
horseshoe
vortex
"I could feel my wingman
coming up behind me.“
- Les King, jet pilot
Formation Flight – Which is easier : Flying solo or leading a formation?
White Pelican migration, Cibola Nature Preserve, CO River
Notes: As a brief introduction to our empirical lifting line model, let’s first checkout the power and versatility of its key component, the horseshoe vortex. For this flight of white pelicans, does the lead bird enjoy a benefit of leading the formation, versus flying solo? ● Let’s overlay a horseshoe vortex on the lead bird’s wingman, where we find that the wingman’s bound vortex ● and closest trailing vortex ● together generate upwash at the lead bird.
...
Group L/D is enhanced about 9% by flying in formation, any bird toward the front can feel a wingman coming up from behind.

## Slide 19
Underground mirror image
Ground Effect, courtesy of Albert Betz
Image mutual effects
Upwash at the wing
Upwash at the tail
Negative “streamwash”
+25% L/D
By permission, GettyImages.com
Albert Betz
Notes: The aeronautical world is much indebted to Albert Betz, arguably Ludwig Prandtl’s most practical and productive protégé. Betz brought forth in the first half of the 20th century numerous advances in aerodynamic analysis of wings, propellers, and wind turbines, including his empirical discovery of the subsonic benefits of wing sweep.
Early in the 20th century he discovered that ground effect can be modeled with a mirror image inverted “virtual aircraft” beneath the ground or water. ● Modeling both wings with equal but opposite horseshoe vortices, ● we find that the image vortex induces not only upwash at both the wing ● and tail, ● but also a negative streamwash, ● whereby groundspeed and airspeed differ when the aircraft generates lift during takeoff or landing.

## Slide 20
Ground Effect
Brown Pelican, San Pedro, CA
Notes: This brown pelican, gliding in ground effect with its wingtips a few centimeters off the water, enjoys a significant reduction of drag relative to flight in free air.

## Slide 21: Empirical lifting-line method
Bound. cond.: Equiv.-plate-parallel flow
Horseshoe
vortices
Lifting-equivalent
Thin, flat airfoil
n ≡ a + z
Cambered airfoil
chord line and
zero-lift incline.
z
a
Planar or
non-planar
Half wing
Downwash line
Lifting line
Shift both L’line & d’line aft if transonic
Stretch L’line_to_d’line gap if transonic
All inputs and outputs are streamwise
Solve linear system for vortex strengths
Notes: Our empirical lifting line method aligns multiple horseshoe vortices on all lifting surfaces with the vortices anchored to the quarter-chord line. ● An equal number of downwash nodes are initially positioned at ¾-chord. ● If the flow is transonic, both lines are shifted aft, ● and then stretched apart ● by a factor obtained by applying the Helmbold-Polhamus Condensation twice, first at zero Mach number and second at flight Mach number. We solve a linear system of equations for the strengths of all vortices, ● each mutually affecting all others, subject to the boundary condition of flow parallel to the equivalent-flat-plate airfoil. ●
...
Local incidence is determined with two vector operations, the first a cross product of the chord and flight-velocity vectors to yield the magnitude of incidence, and the second a cross product with the local “unit dihedral” vector to determine the sign of the incidence.

## Slide 22: Empirical lifting-line validation: Wing & forebody lift distributions
body taps
Notes: This represents the first of several cases hoping to validate our empirical lifting-line method. This wing-body model, tested at Mach 0.9 ● by NACA engineer Jack Runckel, had an axi-symmetric body and 4%-thick symmetric section. Pressures were measured on the exposed wing and on the portion of the body enclosing the submerged wing. ● For our lifting-line analysis, the forebody planform is slightly elevated above the wing to avoid trailing-vortex interference. ● Although the forebody planform is modeled as a low-aspect-ratio wing, ● the afterbody planform is not modeled because it is immersed in low-quality flow and wing downwash. ● Either small dome at upper right ● represents forebody lift which, combined with the calculated and measured wing lift, gives a nearly elliptical wing-body lift distribution. ● As a sanity check, the area under the curve at top center must be unity for any planar half wing. ● At lower right, the -4.5o upwash at the wingtips cancels the 4.5o angle of attack.
.....

## Slide 23
Saab Viggen (Thunderbolt)
SaabGroup.com
23
Notes: We’ll next apply the method to the Saab Viggen (Thunderbolt) delta-canard fighter of the 1960’s. Notice for both the wing and canard the leading-edge droop which mitigates or eliminates thin-wing lift and drag “breaks” at about 4o angle of attack.

## Slide 24
Lifting-line Model of Saab JA37 Viggen (Thunderbolt)
Notes: Here we study the aerodynamic forces and moments on the Saab Viggen cruising at 0.90 Mach number. ● We will trim the aircraft in pitch with an assumed 10% static margin, ● noting that such margin will be reduced at low speed. With the two-position canard flap up for cruise, the canard has 1o decalage ● for zero pitching moment about the vehicle c.g. ● Wing elevons are then used to control pitch, as was the case with the Viggen’s predecessor, the Saab Draken. ● At upper right are measured and calculated distributions of lift for the wing, canard, and forebody. ● And toward the right we find the canard to be working much harder than the wing. ● All of today’s Eurocanards fly with negative static margin, thus substantially reducing the load on the canard, with the canard now controlling pitch. Nevertheless, the Viggen was truly a configuration pioneer.
.....
In setting the decalage of a contemporary canard, such as that of the Saab Gripen, we encounter the question of how best to model the decalage of the “submerged canard” (local body). Although the body of course remains fixed as the exposed canard incidence is varied, the surface pressures on the exposed canard will “carry over” to a certain extent onto the body. This smoothes out the system lift distribution.

## Slide 25
C-17 over San Pedro, CA 4th of July, 2011
Winglets

## Slide 26
Winglet Study: NASA TN D-8474
Notes: Here our empirical lifting line model has been applied to study a wind-tunnel model of a transport aircraft cruising at Mach 0.78 and 3.5o angle of attack. ● In the middle we see the centerline empirical shaping of the lifting line, as well as the empirical aft shift of both the lifting and downwash lines for transonic conditions. ● In the front view at lower left we define a projected distance (p) along the spar, as a fraction of the halfspan (h) which is measured in the plan view. ● For this aircraft equipped with winglets, (p/h) equals 1.1 at the winglet tip. ● At upper right we show good agreement between predicted and measured lift distributions. ● At lower right we discover the upwash, ● actually “normalwash” acting on the winglets, giving rise to local aerodynamic thrust, ● even though the winglets are uniformly toed out 4o. When I presented these results to a local engineering chapter, one attendee sarcastically stated that he intended to power his home-built aircraft with winglet thrust. Shortly following our discussion next of wing sweep, we will show how we can determine the local upwash and local drag.

## Slide 27
Forebody
Configuration Aerodynamics – Classical Methods Applied
Theorists
GettyImages.com
Foil para. geom.
Apply
Emp. L’line
L. edge thrust
App. upwash
Elliptic wing
Sweep
Foil empirical
Wing empirical

## Slide 28: Effect of sweep on zero-lift drag ~ infinite swept wing
c
n
dy
ds
dDp
dNp
L
n
v
a
dL
w
dL
Notes: This sketch represents our own analysis of the well-known swept-infinite wing, where we translate to streamwise the “spar-normal” lift slope, lift coefficient, and pressure drag coefficient. These respectively are seen to apply the first, second, and third powers of the cosine of the sweep angle(L). ●●● For an airfoil at low speed, pressure drag can be ignored in comparison to friction drag. And for a given wetted area, wing sweep has little effect on friction. Thus at low speed sweep reduces lift, but it does not reduce the drag. At transonic conditions, however, pressure drag quickly becomes dominant, as confirmed with Albert Betz’ test data which we study next.

## Slide 29: Historic wind-tunnel test data – the swept wing
Compare friction & pressure drag constituents and apply swept-wing principles to understand this data
Albert Betz
by permission, GettyImages.com
Notes: On the eve of WWII, and following Adolf Busemann’s theoretical discovery of sweep benefits in supersonic flight, Albert Betz empirically discovered the benefits of sweep for subsonic flight. His historic wind-tunnel test data is shown in this slide. Betz tested straight and swept wings ● with the same aspect ratio and streamwise symmetric airfoil of 12% thickness ● at 0.8 Mach number. Zero-lift drag was reduced by 45% with sweep. ● To understand these test results we must isolate friction drag from pressure drag, and we do that next. ●

## Slide 30
NACA high-speed test data: Symmetric airfoil drag at zero lift
cdf
cdp
Zero-lift drag at Betz’ Test Conditions
Notes: Here we re-visit data representing symmetric airfoil transonic drag rise at zero lift. The “floor” of the plot represents friction ● only weakly affected by thickness or Mach number. But pressure drag, typically insignificant at low speed, becomes dominant in transonic flow. ● For Betz’ test conditions, streamwise we had 0.80 Mach and 12% thickness. ● Normal to the spar we had 0.66 Mach and 15% thickness. ● Constructing a table of the various drag constituents, ● and recalling the sweep-cosine-cubed factor on pressure drag, we can “post-predict” the reduction of zero-lift drag afforded by wing sweep.
.....
As hinted earlier, a wing with a symmetric section of 12% thickness (t/c) at Mach 0.8 will likely suffer “transonic treachery.” Here we draw from our suggested notion of apparent thickness (twice the upper-half thickness, or more-precisely 2Zmax) which, to be safe, should be perhaps 6% or less for the flight regime tested by Betz. Today’s transport aircraft use inverted camber near the wingroot, whereby the lower half of the airfoil can safely provide structural depth as the upper half of the airfoil gives the appearance of a thin section to the transonic flow.

## Slide 31: Early implementations of wing sweep
ME 163
pitch trim
Ho 229
Sweep & twist for pitch trim
Saab J-29Tunnan – 1st use of Betz’ data
World’s first area ruling
Saabgroup.com
Mario Merino
ME 262 – sweep for c.g.
Betz’ Rep. / Allies
Notes: Although Betz’ discovery of reduced drag with sweep occurred in 1940, the Germans did not directly apply it. The Me-262,● appearing in the last year of the war, incorporated sweep only to manage c.g. position. Both the Me-163 ● and Horten 229 ● applied sweep with twist only to trim the aircraft in pitch. The post-war Saab J-29 Tunnan, ● which did not incorporate wing twist,* was the first operational jet to directly apply sweep to reduce drag. But it was early in the war that the Swedes got a copy of Betz’ test report on sweep. ● When they shared it with the Allies, the response was “not interested.” The J-29, was also ahead of its time with the world's first application of area ruling. ● This no doubt led to the J-29 "barrel" nickname, and arguably served to discredit the popular phrase "It has to look good to fly good.“
* Sept 2013 e-mail from Lars Helmersson, Principal Engineer (Ret.) Saab Aeronautics

## Slide 32
Forebody
Configuration Aerodynamics – Classical Methods Applied
Theorists
GettyImages.com
Foil para. geom.
Apply
Emp. L’line
L. edge thrust
App. upwash
Elliptic wing
Sweep
Foil empirical
Wing empirical

## Slide 33
Two Elliptical Wings - Drag due to Lift Vs. Theory
pAcDL
Square of Lift Coefficient, cL2
10% underprediction of drag due to lift
Data
Prandtl Theory
cDL = cL2/(pA)
Notes: As motivation for this part of our study, we first show that Prandtl’s prediction of drag due to lift falls about 10% below NACA and NASA test data ● for two elliptical wings. We postulate that a shortfall in leading edge thrust is partly to blame, as Prandtl had unknowingly assumed full leading-edge thrust in his pioneering analysis. ● Another contributor may be Prandtl’s decision to evaluate both lift and downwash at the quarter-chord lifting line, whereas follow-on researchers took more of a lifting-surface approach by evaluating downwash at three-quarter chord. Whatever the cause, we will now attempt to get closer to the test data by first introducing an empirical characterization of leading-edge thrust, and then introducing our apparent upwash method for drag due to lift. ●

## Slide 34
Dynamic Soaring
Wing aspect ratio ~ 15
3-g turn every 20-seconds
Zoom upwind, dive downwind
Terrain following, half asleep
Lower 10-m of 20-m b’layer
Any net direction w/o flapping
6X / year
www.HowFliesTheAlbatross.com
Notes: Although Prandtl underestimated drag due to lift, his pioneering analysis brought us a first understanding of the advantages of high aspect ratio. The wandering albatross ● has for over 50-million years evolved and employed a high-aspect-ratio wing ● to substantially reduce drag due to lift as it undergoes a 3-g dynamic-soaring maneuver every 20-seconds, ●● including terrain following among the waves, often while half asleep. ●● Exploiting the lower 10-m of a 20-m wind boundary layer, the albatross employs intelligent maneuvering to progress in any net direction on shoulder-locked wings, although overall it circumnavigates Antarctica several times per year. ●
After 50-million years of gracing our blue planet, the albatross has just over the last century suddenly neared extinction due to floating plastic at sea, long-line fishing, and invasive species on the remote islands where it nests on the ground. For a concise explanation and real-time simulation of albatross dynamic soaring, visit www.HowFliesTheAlbatross.com

## Slide 35
Leading-edge thrust and drag due-to-lift in 2-D flow
Next, get f from test data →
Assumptions and Definitions:
n ≡ eq._plate net 2D incidence = a+z
cla ≡ Lift slope ≡ dcl /da = cl / n ≈ 2p
f ≡ fraction of equiv._plate (cdL = n cl )
Thus: cdL ≡ cd - cdo = f n cl = (f/cla) cl2
With camber: cdL ≈ (f/cla) (cl - cla z)2
ct ≈ ncl ; cdL = 0
“perfect” foil
Pressure
integrated
resultant is
normal to vo
cn ≈ clan
cdo
n
vo
a
z
n
cl ≈ cn
ct ≈ 0 ; cdL ≈ ncl
n
Pressure
integrand
normal to
equiv.plate
vo
n
cdo
“plate” foil
cn ≈ clan
cl ≈ cn
Typical foil
cn
cl
cdL = fncl
cdo
vo
a
z
n
Pressure
integrand
f ≈ constant if cd (cl) is parabolic
Notes: To evaluate 2D drag due to lift, let’s first define a net incidence (n) ● as the sum of the angle of attack (a) and zero-lift-line inclination (z). Then at low speed, all airfoils will develop a chord-normal force coefficient (2pn).
A typical thick and lifting airfoil has a stagnation point below the chin, and upflow across the nose with a strong drop in pressure. Here, a “perfect” foil will develop the maximum available leading-edge thrust combining vectorially with the chord-normal force to develop a vertical pressure-integration force which, for the perfect foil, becomes the lift. ●
If, however, the airfoil is instead flat and ultra-thin, ● it has no frontal area with which to develop leading-edge thrust, whereby the pressure-integration vector stands normal to the chord. The corresponding coefficient of drag due to lift is approximated by the product of lift coefficient and net incidence.
For a “real” airfoil, situated between the two previous extremes, ● we can say that the actual drag due to lift is some fraction (f) of the flat-plate drag due to lift. The related arithmetic ● reveals that (f) will be constant to the extent that the airfoil drag polar can be fit with a parabola, as is often the case. ●

## Slide 36
2D drag due-to-Lift ~ New analysis of NACA high-speed test data
t/c = 0.0
n
d
d
Only thick wings
approach Prandtl
drag due to lift
Now define
l  1- f
Notes: Here we characterize NACA test data representing symmetric airfoil drag due to lift as a fraction (f) of the flat-plate reference, as thickness and Mach number vary. As expected only relatively-thick foils approach the ideal (f=0). Here we’ll take the opportunity to define the companion parameter (l=1-f) representing the attained fraction of maximum available leading-edge thrust.
....
Incidentally, NACA aerodynamicist R.T. Jones applied the term leading-edge thrust in his book “Wing Theory,” and such thrust is often parallel to engine thrust.

## Slide 37
Apparent upwash method: Leading-edge thrust & 3D drag due-to-lift
Positive upwash increases thin-foil drag but decreases thick-foil drag
n ≡ 2D net incidence = a+z
u ≡ apparent upwash = (cl /cla ) - n
f ≡ fraction of limit cdL= (n+u) cl
l ≡ 1 - f = fraction of limit ct = ucl
cdL ≡ cd - cdo = f (n+u)cl - lucl
= (f/cla) cl2 - lucl symmetric foil
≈ (f/cla) (cl - cla z)2 - lucl camber
Given cl via Lifting-line solution,
and foil properties & conditions, solve for apparent upwash, u
and local drag due to lift cdL
u
lucl
f(n+u)cl
cdo
vo
a
cl
cn
z
n
u
n
cl ≈ cla(n+u)
apparent upwash
u ≡ (cl /cla ) - n
Notes: Here we expand upon the previous 2D analysis to include the effects of the local upwash angle (u) in 3D flow. Positive upwash will typically apply at forebodies, canards, nacelles, winglets, and raked wingtips. Everywhere else upwash will be negative. The diagram above enjoys considerable simplification by showing the case of positive upwash.
First and foremost, the lift is proportional to total incidence.● Given the total incidence, lift slope, and lift coefficient solved by our lifting line, we can deduce the apparent upwash angle (u). ● Next assuming positive upwash, the pressure-integrated force vector is lengthened, and to the extent that the airfoil is flat and thin, it leans back with increased drag. ● To the extent that the airfoil is thick, it will incrementally lean forward, reducing drag. ●
Throughout this discussion we have borrowed the force-leaning concept introduced by Prandtl. However, only if the airfoil enjoys full leading-edge thrust, an assumption made unknowingly by Prandtl, can the airfoil be credited with fully leaning forward. ● If upwash (u) is locally zero, the 3D drag due to lift reduces to the 2D basis derived earlier herein.

## Slide 38
Drag due to lift validation, elliptical wing
Incl. foil, Abbott & Doenhoff, p. 463
Prandtl: cL2/(pA)
Notes: The elliptical wing of the figure above constitutes our first test of our method, seen to exhibit a good match with test data. Note the shortfall in predicted drag with Prandtl’s formula, even after adding the NACA 0012 drag polar from Abbott & Doenhoff. Here we recall that Prandtl’s method assumes full leading-edge thrust (l=1), a condition approached only by relatively-thick wings.

## Slide 39
Drag due to lift validation Proposal: Run all four cases with CFD
Notes: Here the elliptical wing test article joins three others for a representative comparison of our predicted drag due to lift versus measured drag due to lift. We invite those interested to run all four cases with CFD to compare low-order and high-order computational method results.

## Slide 40
Forebody
Configuration Aerodynamics – Classical Methods Applied
Theorists
GettyImages.com
Foil para. geom.
Apply
Emp. L’line
L. edge thrust
App. upwash
Elliptic wing
Sweep
Foil empirical
Wing empirical

## Slide 41
2040+ service entry
Ultra-bypass/open rotor
Noise shielding
Aero-elastic stabilized
Flight-continuous APU
B’layer ingest./manip.
L/D ≈ 22
www.NASA.gov
Future Transport
Notes: We’ll now wrap up the presentation by applying the previously-described principles and methods to estimate the aerodynamic characteristics of this advanced transport in cruise.

## Slide 42
Lifting-line Model ~ Boeing blended wing-body
Notes: The Boeing blended wing-body transport concept exhibits several interesting aerodynamic phenomena. It would cruise ● at 11-km altitude, Mach 0.8, and a=6o. The centerbody ● has a positive pitching moment which, together with wing sweep and twist, trims the aircraft with 8% static margin. The wing twist distribution ● includes 5.5o washout at the raked wingtip. Empennage is toed out 2o. The wing lift distribution ● is more half-sinusoidal than elliptical. Characteristic of a blended wing-body, ● the lift coefficient dips in the center. The root-to-tip variation of empennage lift ● suggests that the empennage should be twisted to mitigate its contribution to induced drag. Finally at lower right ●● we see the upwash and attendant thrust of the raked wingtips.
Whereas today's airliners can cruise at L/D approaching 20, this concept can cruise near L/D=22. However you may be surprised to learn that maximum L/D is reserved for climb and loiter ; for optimal cruise (specific range) we instead maximize the square root of cL over the first power of cD, and that means flying faster than we would for max L/D.

## Slide 43
Lifting-line Model ~ Lockheed boxwing
CG
AC
Aft
Fwd
Aft
Fwd
Aft
Fwd
Fwd
Aft
Notes: We conclude our study by estimating basic aero characteristics of the Lockheed-Martin Boxwing transport. Cruising near 0.8 Mach at a=5o, ● it employs relatively high-aspect-ratio, swept joined wings which will likely require aero-elastic stabilization. Assuming a positive static margin, ● the forward wing will have a higher incidence than the aft wing as shown at lower left. ● Optimizing forward wing, aft wing, and endplate twist, not done in this exercise, will certainly be a challenge. A large fin ● will be needed to overcome forebody side force and other yaw-destabilizing effects. At upper right, ● the forward wing carries higher lift than the aft wing. At middle and lower right, ● the aft wing induces upwash on the outboard portion of the forward wing.

## Slide 44
Forebody
Summary: Configuration Aerodynamics – Classical Methods Applied
Theorists
Foil para. geom.
Apply
Emp. L’line
L. edge thrust
App. upwash
Elliptic wing
Sweep
Wing empirical
GettyImages.com
Notes: We reviewed and renewed the work of visionary classical aerodynamicists on linear, longitudinal configuration aerodynamics. ● The power of the cubic spline for existing or new airfoil parametric geometry modeling was demonstrated. ● We showed that Prandtl's formulations for lift and drag, although pioneering, were both optimistic. ● Enhanced accuracy of wing lift was then provided by the Helmbold-Polhamus Condensation adding sweep and transonic effects. ● We then introduced an empirical correlation of leading-edge thrust, together with our Apparent upwash method, to characterize drag due to lift. ●
We also reviewed the low-aspect-ratio wing principles derived by Munk and Jones, ● and explained Betz' historic discovery of subsonic benefits of sweep. Our Empirical lifting line ● was applied to show spanwise distributions of lift and drag on conventional and new configurations, highlighting the aerodynamic thrust of winglets and raked wingtips. ● For the future, we urge young aerodynamicists to recall and apply any or all of these fundamentals before turning to computational fluid dynamics to further refine their aircraft configurations.

## Slide 46
J. Philip Barnes has a Master’s Degree in Aero Engineering from Cal Poly Pomona and Bachelors Degree in Mechanical Engineering from the Univ. of Arizona. As a 40-year veteran of air vehicle and subsystems performance analysis at Northrop Grumman, he supports mature and advanced tactical aircraft programs. Author of many SAE and AIAA technical papers, and often invited to deliver travel-paid lectures at various universities, Phil sometimes mentors university teams working capstone projects, and the fruits of such collaboration have appeared in his recent technical papers.
Outside of work, Phil is one of the world’s top experts on wandering albatross dynamic soaring, and he is pioneering the science of regenerative-electric flight. Phil’s work has been characterized by faculty and colleagues as “landmark” and “inspiring to many,” and he was named Cal Poly Pomona Engineering Alum of 2014, where he presented “Future Flight: Learning From the Birds” to an audience of two hundred graduates, family, and faculty.
About the Author